## Slide 1
A team can have up to 4 members including the team leader. Add rows if necessary.
Team Details
Team Name:
SR. NO
ROLE
NAME
ACADEMIC YEAR
1
Team Leader
2
Member 1
3
Member 2
COLLEGE NAME
TEAM LEADER CONTACT NUMBER
TEAM LEADER EMAIL ADDRESS
Zynq
Adithyan B
4 th year
Arpith Alex
4 th year
Navaneeth Thushar
4 th year
Saintgits College Of Engineering
+91 79073342255
adithyxn05@gmail.com

## Slide 2
Problem Statement Addressed
AI-Based Restoration of Degraded Images for Semiconductor Inspection
DESCRIPTION / DETAILS
Problem Statement: Reconstruct degraded 128 x 128 noisy wafer images to 256 x 256 high-resolution ground-truth structures.
Domain Context: Fast optical/SEM semiconductor inspection scans suffer from severe photon noise, speckle noise, and diffraction limits.
Industry Significance: Enables high-speed wafer inspection and accurate defect detection without expensive hardware upgrades or reduced fab throughput.

## Slide 3
Idea Description - Describe your Idea/Solution/Prototype
KEY CONCEPT & APPROACH
A lightweight, activation-free super-resolution network (NAFNet-SR) using sub-pixel convolution and a multi-domain composite loss (spatial, structural, spectral, and perceptual) to restore 128 x 128 noisy wafer images to 256 x 256 high-resolution ground truth at real-time inspection speeds.
SOLUTION OVERVIEW
NAFNet-SR uses a lightweight 2.39M-parameter activation-free architecture with sub-pixel convolution and multi-domain loss to restore degraded 128 x 128 wafer inspection images to 256 x 256 resolution at real-time speeds (127.5 FPS).

## Slide 4
Proposed Solution - Describe your Idea/Solution/Prototype
SOLUTION DETAILS
Core Idea & Methodology: Reconstructs degraded 128x128 wafer inspection images to 256x256 ground truth using NAFNet-SR, an activation-free deep residual architecture with sub-pixel convolution.
Data & Signal Pipeline: Processes raw Float32 unclipped grayscale images to preserve physical sensor noise dynamics (shot/thermal/speckle noise) without clipping artifacts.
Loss & Optimization: Trains on a multi-domain composite loss combining Charbonnier (spatial), SSIM (structural), 2D-FFT (frequency pitch lines), and LPIPS (perceptual) objectives.
Technologies Involved: Built using PyTorch 2.0+, CUDA 12+, torch.fft, Sub-Pixel Convolution (PixelShuffle), and LPIPS.
Problem Addressal & Impact: Restores fine nanoscale conductor edges and eliminates noise at real-time speeds (127.5 FPS with 199.5 MB VRAM), avoiding costly hardware upgrades.

## Slide 5
Innovation and Uniqueness
KEY INNOVATION
Innovation Type: A novel process & application combining parameter-efficient AI super-resolution with physical sensor signal preservation for semiconductor inspection.
Core Technical Approach: Uses a 2.39M-parameter activation-free network (NAFNet-SR) with unclipped Float32 raw data ingestion and 2D-FFT spectral loss to recover fine pitch lines.
Fab Impact: Enables real-time restoration of sub-nanometer wafer structures (127.5 FPS at 199.5 MB VRAM) without expensive physical hardware modifications.
COMPETITIVE ADVANTAGE
Efficiency: 6.6× parameter reduction (2.39M params) with a minimal 199.5MB VRAM footprint for edge inspection deployment.
Performance: Outperforms bicubic baselines (+5.15 dB PSNR) by restoring nanoscale conductor edges without high-frequency blur.
Cost & Usability: Delivers real-time inline throughput (127.5 FPS) as a pure software upgrade, avoiding multi-million-dollar physical sensor replacements.

## Slide 6
Impact and Benefits
Primary Impact
Primary Impact: Maximizes semiconductor wafer yield by restoring sub-nanometer defect clarity (+5.15 dB PSNR) to prevent false alarms and missed critical defects.
Cost & Scalability: Serves as a zero-hardware-cost software multiplier, eliminating multi-million-dollar physical sensor and optical lens replacements.
Inline Fab Performance: Processes scans at 127.5 FPS with a minimal 199.5 MB VRAM footprint, seamlessly integrating into continuous real-time inspection pipelines.
Quantifiable Outcomes
2x Super-Resolution (4x Pixel Density): Upscales 128x128 noisy scans to 256x256 high-resolution ground truth.
+46.5% Structural Accuracy Boost: Improves SSIM from 0.528 to 0.776 (+5.97 dB PSNR gain over bicubic baseline).
40.3% Perceptual Error Reduction: Reduces LPIPS feature distortion from 0.443 down to 0.264.
6.6x Model Efficiency: Reduced parameters to 2.39 M with ultra-low 199.5 MB VRAM footprint at 127.5 FPS throughput.

## Slide 7
Technology & Feasibility/Methodology Used
IMPLEMENTATION STRATEGY
Technical Stack (Software & Hardware): PyTorch 2.0+, CUDA 12+, Python 3.10+, torch.fft, and LPIPS; evaluated on edge GPU hardware (NVIDIA RTX 3050).
Architectural Approach: NAFNet-SR (2.39 M params) utilizing parameter-free SimpleGate activations, Simplified Channel Attention (SCA), and PixelShuffle 2x sub-pixel convolution.
Loss Optimization: Multi-Domain Composite Loss combining Charbonnier (spatial), SSIM (structural), 2D-FFT (frequency), and LPIPS (perceptual) objectives.
Feasibility & Production Integration: Operates at 127.5 FPS with an ultra-low 199.5 MB VRAM footprint, making it immediately feasible for real-time inline fab deployment without hardware changes.

## Slide 8
GitHub & Video Link
GitHub Repository
https://github.com/Ad1thh/KLA-Semicon-AI-Restoration
Prototype / Simulation Video
https://github.com/Ad1thh/KLA-Semicon-AI-Restoration/blob/main/assets/DemoVideo.mp4